## Slide 1: Performance 1: Overview & Latency
Source of most materials:
Xiwei Xu, Ingo Weber, and Mark Staples. Architecture for Blockchain Applications. Springer, 2019

## Slide 2: What will you learn this week?
Performance Overview
Latency
  Transaction Inclusion in Public Blockchain
  Simulating Latency
Throughput

## Slide 3: Performance Overview

## Slide 4: ISO/IEC 25010:2011 Quality Model
Functional suitability
Functional correctness
Functional complete-ness
Performance efficiency
Capacity
Resource utilization
Functional appropriate-ness
Time behavior
Compatib-ility
Interop-erability
Co-existence
Usability
Operability
User error protection
Reliability
Availability
Recoverab-ility
Maturity
Fault tolerance
Security
Integrity
Confidential-ity
Non-repudiation
Accountab-ility
Authent-icity
Maintain-ability
Modularity
Reuseability
Modifiab-ility
Testability
Analyzab-ility
Portability
Installability
Replace-ability
Adaptability
Notes: International standards for evaluation of software quality
Blockchain has good and bad quality

## Slide 5: Performance-Related Considerations
Load
Resources
Performance
Resource Utilization
System
Efficiency
Network
Memory
CPU
Disk
…
Latency
Throughput
Timeliness
…
Scalability
Capacity
Bottlenecks
Background
Sustained
Increasing
Stress
Standard benchmarks
Representative?
Production
…
Notes: 10. Performance

## Slide 6: Some Important Varieties of Performance
Latency
  How quickly does the system respond to a request?
Throughput
  How many requests can the system process in a fixed unit of time?
Timeliness
  Will the system always process a request in a specified time window?
Scalability is an orthogonal issue
  How does <performance> change under increasing load & system resources?
    (Can also be about the response of a system when decreasing resources, under variable load)

## Slide 7: To Understand Performance, You Need Measurements
Application-Level measurements
  Overall performance; check requirements met; validate results from detailed models
Component-Level measurements / Micro-benchmarking
  Piece-wise drivers of performance; observe interactions; identity bottlenecks
Load testing – check system response & utilisation under increasing load
Stress Testing – check maximum capacity; find resource bottlenecks
Soak Testing – check system response under long-duration load
“Benchmarking crimes” – what not to do:
  https://www.cse.unsw.edu.au/~gernot/benchmarking-crimes.html

## Slide 8: Predicting Performance?
Analytic formulae
  Highly abstract/simplified models
  Quick & dirty
  Only needs design & component benchmarks
  Can be done before developing the system
Simulation
  Uses a model; many abstractions/simplifications
  Only needs a design & benchmarks, but takes work
  Starts to explore variation & interactions
  Can be done before developing the system
Monitoring
  Needs real deployed system
  Needs a monitoring framework
  Most valid results; e.g. actual effects!
Needs a real deployed system
Only needs a design & benchmarks
Highly approximate
Most valid results

## Slide 9: Some Resources in Blockchains
For public blockchains
  Cryptocurrency for Transaction Fees
    Can affect probability of transaction inclusion (impacts transaction latency)
  Mining difficulty for Proof of Work
  Gas & Block Gas Limits (e.g. in Ethereum)
    More of an Availability problem as discussed in lectures on dependability and security
  Network capacity including speed of light for global transaction & block propagation
    Impacts consensus for transaction inclusion latency
  Transaction throughput capacity
    Latency will be impacted when system is overloaded beyond capacity
For private blockchains / running a node for a public blockchain
  Normal cloud/enterprise server & network resource considerations
  …and most of the above, depending on blockchain configuration

## Slide 10: Latency

## Slide 11: Transaction Inclusion Time in Public Blockchain…
t1
Tx sent
t2
miner includes Tx in candidate block
interblock time
t3
Tx is observed in new mined block
interblock time / 2
t0 start mining on previous candidate block
+
Timeline
(not to scale)
mining
mining

## Slide 12: Student Task
How long does it take to get a transaction committed in Bitcoin?
  Assume 10 minutes interblock time and 6 confirmations

## Slide 13: … Plus Extra Small Bits of Time
t1’
Tx arrives at miner
t1
Tx sent
t2’
miner includes Tx in new candidate block
t3
block is mined
interblock time
(includes block prep time)
t3’
Tx is observed in new block
interblock time / 2
t0 prev candidate block
t2
block is mined
Timeline
(not to scale)
+
+
+
Tx propagation time
block propagation time
+ block prep time
https://ethstats.net/

## Slide 14: … Also, Major Sources of Variation in Latency
t1
Tx sent
t2
miner includes Tx in candidate block
t3
Tx is observed in new mined block
t0 start mining on previous candidate block
Timeline
(not to scale)
Probability of Tx inclusion? May have to wait for another block. Also, affected by fees…
Arrival time within mining window?
Previous interblock time?
Current interblock time?

## Slide 15: Upshot is High Variation of Latency
On Ethereum: not 1.5 x interblock time; in practice more like ~1.8 x inter-block time?
But with a lot of variation! Some caused by Tx fee, gas fee, etc.
You need to design your system to cope with this to meet requirements
N.B.: 11 “confirmation blocks” add a large
“constant”-ish factor on the main cause of difference
in latency variation
Notes: Even though blockchain replace the need of trusted third party, the latency of blockchain can be a major drawback. In a blockchain using Nakamoto consensus, to confirm a transaction, it needs to be included in a block, which should be endorsed by dependent blocks, known as confirmation blocks.
On Bitcoin the inter-block time is about 10 minutes and 6 confirmation blocks are often used while on the public Ethereum blockchain the average block generation time is about 15s and 12 confirmation blocks are typically recommended. As you can see, the latency incur to the system will be high in magnitudes.
Additionally, Transaction delays can also arise from network delays, the transaction fee offered, the number of transactions being processed, and the strategic decisions made by miners. So, transaction inclusion times can vary widely.
Although longer than in conventional systems, these transaction latencies may be acceptable for some use cases. it will still be important to be able to accurately predict system-level latency during the design phase, to assess the impact of this limitation on system requirements

## Slide 16: An Aside: Transaction Inclusion with Proof of Authority in Private Blockchain
t1
Tx sent
interblock time / 2
t0 previous block
Timeline
(not to scale)
t2
“miner” includes Tx in candidate block
t3
Tx is observed in new block
Assuming transaction arrives before the small window near end of interblock time where the next block is constructed by the Authority, i.e. t1 < t2
This can be tricky because interblock time tends to be much smaller in private blockchains, but tends to have much lower transaction latency anyway
(no or few confirmation blocks)

## Slide 17: In Public Blockchains, Wait for Confirmation Blocks
Nakamoto consensus can create “uncle” blocks
  Blockchains using Proof-of-Work, Proof-of-Stake, …
  Transaction you saw in a block turns out not to have been officially included in the blockchain (not in main chain, only in uncle block)
  Only probabilistic, long-run, transaction commit
Can increase confidence your transaction is really included, by waiting for subsequent “confirmation blocks”
  For Bitcoin, often people say wait 6 blocks
  For Ethereum, often people say wait 12 blocks
    (Lower interblock time can increase likelihood of uncles)
Waiting for confirmation blocks increases latency, and increases latency variability
  But increases confidence in finality

## Slide 18: Confirmations: Inclusion Confidence vs. Latency
Should be risk-based: how much confidence vs. how much latency?
“Analysis of hashrate-based double spending”
https://arxiv.org/abs/1402.2009

## Slide 19: Confirmations: Inclusion Confidence vs. Latency
Should be risk-based: how much confidence vs. how much latency?
“On Availability for Blockchain-Based Systems”
https://research.csiro.au/data61/wp-content/uploads/sites/85/2016/08/OnAvailabilityForBlockchain-BasedSystems-SRDS2017-authors-copy.pdf
“Analysis of hashrate-based double spending”
https://arxiv.org/abs/1402.2009
0.1  10% of hashrate
Blue line: 0.1% chance of successful double-spend
confirmation blocks: 6

## Slide 20: Student Task
How can architects influence Tx latency?

## Slide 21: How Architects Can Influence Transaction Latency
Offer a Transaction fee that meets/exceeds miners’ expectations
  Ethereum “fee” is gas price * gas used
  Gas price is user-defined
Choose smallest number of confirmation blocks that is “safe” for your application
Use another blockchain (private? or a public blockchain that works “better”?)
  Configure blockchain to use other consensus algorithms (PBFT, PoA, …)
    Avoid Nakamoto consensus & possibility of uncles, so you can avoid confirmation blocks
  Configure blockchain to target a small interblock time
Work off-chain, e.g. using “state channel” design pattern, to be discussed in later lectures

## Slide 22: Performance 1: Overview & Latency
Source of most materials:
Xiwei Xu, Ingo Weber, and Mark Staples. Architecture for Blockchain Applications. Springer, 2019